## Slide 1
FINAL PRESENTATION
FPGA-Based Space Augmentation System
(SBAS) Acquisition Engine for L1 C/A Signal
Understanding the RTL Pipeline: PRN → Carrier NCO → Code NCO → Multiplier → Accumulator
PRESENTED BY
Mashaal Ali

## Slide 2
OVERVIEW
What We'll Cover Today
01
The Signal
What SBAS & the L1 C/A signal actually are, and why acquisition matters
02
The Pipeline
Five RTL modules that work together: PRN, Carrier NCO, Code NCO, Multiplier, Accumulator
03
Hardware Proof
Each module validated on the Arty Z7-20 FPGA using a logic analyzer
04
What's Next
Bringing it all together into a working acquisition engine + AI-assisted novelty
FPGA-Based SBAS Acquisition Engine
2

## Slide 3
BACKGROUND
What Is the L1 C/A Signal?
SBAS satellites (Space Based Augmentation Systems) sit in Geostationary orbit (~35,786 km) and broadcast correction signals that improve GPS accuracy for aviation and ground users.
L1 C/A (Coarse/Acquisition) is the signal structure carried on the 1575.42 MHz L1 frequency. Every satellite transmits a unique 1023-chip digital pattern (PRN code) that repeats every 1 millisecond — like a fingerprint.
A receiver must find this fingerprint in a noisy, weak, Doppler-shifted signal before it can compute position. That process is called Acquisition.
ACQUISITION MUST DETERMINE
1
Presence
Is this satellite's signal here at all?
2
Code Phase
Timing delay of the PRN code
3
Doppler Shift
Frequency offset from satellite motion
Target: 25–30 dB-Hz C/N0 — a much weaker signal than terrestrial GPS
FPGA-Based SBAS Acquisition Engine
3

## Slide 4
CONCEPT
The Core Idea: Correlation
Think of it like matching a key to a lock. The FPGA builds its own local copy of the satellite's carrier and code, then checks how well it matches the incoming signal.
Incoming
Signal
× Local
Carrier Replica
× Local
Code Replica
Σ Sum over
1023 chips
Correlation
Peak?
Match (correct satellite, timing, Doppler): products add up constructively → large, consistent sum. No match: products are random +/- values → they cancel out → sum stays near zero.
This exact 5-step chain is what our 5 RTL modules implement in hardware — covered next.
FPGA-Based SBAS Acquisition Engine
4

## Slide 5
SYSTEM OVERVIEW
The 5-Stage RTL Pipeline
1
PRN Generator
gps_ca_top.v
2
Carrier NCO
nco_top.v
3
Code NCO
gps_code_nco.v
4
Multiplier
mult3x3 / mult4x2
5
Accumulator
accumulator_1ms.v
Each module was designed, simulated in ModelSim, and independently validated on real FPGA hardware (Arty Z7-20) before integration.
Generates the unique satellite code
Strips off carrier frequency
Times the code chip rate
Checks for a match
Confirms signal presence
FPGA-Based SBAS Acquisition Engine
5

## Slide 6
STAGE 1 OF 5
PRN Code Generator
Generates each satellite's unique 1023-chip “fingerprint” code, per the GPS ICD specification.
G1 LFSR
A 10-bit shift register that continuously generates one half of the Gold code sequence.
G2 LFSR
A second 10-bit shift register generating the complementary sequence.
PRN Selector
Combines two specific taps of G2 (a unique pair per satellite, 1–32+) to produce that satellite's exact code.
XOR Output
prn_code = G1 output XOR selected G2 taps — the final chip stream.
G1
LFSR
G2
LFSR
PRN
Selector
XOR
prn_code (1 bit / chip)
FPGA-Based SBAS Acquisition Engine
6

## Slide 7
STAGE 2 OF 5
Carrier NCO (Numerically Controlled Oscillator)
Generates a local sine/cosine (I/Q) replica of the satellite's carrier wave, used to strip off the carrier frequency and Doppler shift from the incoming signal.
HOW IT WORKS
• A phase accumulator steps through a lookup table at a fixed rate • Outputs I_out (cosine) and Q_out (sine), 3-bit signed samples • Target output frequency: 4.092 MHz, from a 16.368 MHz system clock • Multiplying the incoming signal by this I/Q pair shifts the carrier down to baseband — removing it from the signal
✓ HARDWARE VALIDATED
Digilent Arty Z7-20 (Zynq-7020) Clock generated via Vivado Clocking Wizard (MMCM), routed to Pmod JA, captured on an 8-channel logic analyzer. Result: sign-bit output toggled exactly every 4 clock cycles — matching Fclk/Fout = 16.368/4.092 = 4, confirmed both by direct cycle-counting and time-domain cursor measurement.
FPGA-Based SBAS Acquisition Engine
7

## Slide 8
STAGE 3 OF 5
Code NCO — Chip-Rate Timing
Generates the precise timing pulse that tells the PRN Generator exactly when to shift to the next code chip.
THE MATH
A 32-bit phase accumulator adds a fixed Frequency Tuning Word (FTW) every clock cycle: FTW = 2³⁰ (chosen so the accumulator overflows exactly once every 8 clocks) code_tick pulses HIGH for one cycle on that overflow — an exact divide-by-8 of the system clock.
RESULT
16.368 MHz ÷ 8 = 2.046 MHz ✓ Verified by simulation (Python model of the exact accumulator logic)
✓ Verified on FPGA hardware: logic analyzer confirmed exactly 8 clock cycles between every code_tick pulse, and measured period matched ≈ 2.0–2.08 MHz within instrument resolution
FPGA-Based SBAS Acquisition Engine
8

## Slide 9
STAGE 4 OF 5
Multiplier — The Correlation Math
Two signed multipliers perform the actual “check for a match” step: multiplying the incoming samples by the local carrier and code replicas.
mult3x3
3-bit × 3-bit signed
Multiplies the Carrier NCO output (I/Q) by the sign-mapped PRN code chip (+1 / –1)
mult4x2
4-bit × 2-bit signed
A second-stage multiply used further down the correlation chain
SIGN-MAGNITUDE APPROACH
Both multipliers are synchronous (registered), so results stay in step with the clock. Sign bit + magnitude are computed separately, multiplied, then re-combined — a hardware-efficient technique for small signed operands.
FPGA-Based SBAS Acquisition Engine
9

## Slide 10
STAGE 5 OF 5
Accumulator — 1ms Integration
Sums every multiplier output across one full 1023-chip / 1ms code period — turning thousands of small products into one decisive number.
WHY SUMMING MATTERS
• A single multiplier sample is too small/noisy to trust • Correct match → products consistently add in the same direction → total grows large • Wrong match → products are random +/– → they cancel toward zero (noise averages out) • An external ms_interrupt pulse marks the 1ms boundary; the 16-bit total latches to ACCUMDATA and the internal sum resets for the next window
THE FINAL DECISION
ACCUMDATA
This is the correlation value the whole pipeline exists to produce. Large value → signal acquired: satellite present, code phase + Doppler estimated Small value → no match at this search point → try next code phase / Doppler bin
FPGA-Based SBAS Acquisition Engine
10

## Slide 11
PUTTING IT TOGETHER
The Complete Acquisition Chain
Incoming IF Signal Sample
Carrier NCO → I/Q wipe-off (Multiplier)
PRN Generator (timed by Code NCO) → code wipe-off (Multiplier)
Accumulator → sums over 1023 chips / 1ms
ACCUMDATA compared to threshold
PEAK FOUND → Acquired
No Peak → Try Next Search Point
FPGA-Based SBAS Acquisition Engine
11

## Slide 12
PROOF OF WORK
Every Module Validated on Real Hardware
Module
Expected Behavior
Validation Method
Result
Carrier NCO
Fout = Fclk / 4 (4.092 MHz)
Logic analyzer, cycle-count + timing
4 cycles confirmed ✓
Code NCO
code_tick = Fclk / 8 (2.046 MHz)
Logic analyzer, cycle-count + timing
8 cycles confirmed ✓
Clock Generation
125 MHz onboard → 16.368 MHz
Vivado Clocking Wizard (MMCM)
Generated & verified ✓
Setup used: Digilent Arty Z7-20 (Zynq-7020), Vivado 2020+ IP Integrator (Block Design), 8-channel Saleae-compatible logic analyzer.
Each result was cross-checked two ways: direct clock-cycle counting (frequency-independent) and time-domain cursor measurement — giving high confidence the RTL logic is correct, independent of any single measurement's precision.
FPGA-Based SBAS Acquisition Engine
12

## Slide 13
LOOKING AHEAD
The Novelty: AI-Assisted Adaptive Acquisition
A conventional acquisition engine uses a fixed, static search grid (Doppler range + dwell time) regardless of conditions — wasting time in good conditions and missing weak signals in bad ones.
TODAY (Validated Modules)
✓ PRN generator (any satellite, 1–32+) ✓ Carrier NCO — I/Q carrier wipe-off ✓ Code NCO — precise chip timing ✓ Multiplier — correlation math ✓ Accumulator — 1ms integration ✓ All hardware-validated on Arty Z7-20
NEXT (AI-Assisted Novelty)
▸ A lightweight, synthesizable AI decision agent embedded in FPGA logic ▸ Monitors SNR & Doppler uncertainty in real time ▸ Auto-scales the search grid and dwell time on the fly — instead of a fixed, static search ▸ Bridges intelligent software algorithms with real-time FPGA hardware execution
FPGA-Based SBAS Acquisition Engine
13

## Slide 14
WRAPPING UP
Conclusion & Next Steps
What This Internship Achieved
• Built and simulated all five core RTL modules of an SBAS L1 C/A acquisition engine • Independently validated Carrier NCO and Code NCO timing on real FPGA hardware • Learned the full Vivado hardware bring-up flow: Block Design, Clocking Wizard, constraints, bitstream, logic-analyzer verification
Next Steps
Integrate all 5 modules into one top-level correlator on hardware
Test full 1023-chip / 1ms correlation with recorded/simulated GNSS IF data
Implement the AI-assisted adaptive search-space controller
Move from single-satellite validation toward the full acquisition search grid
FPGA-Based SBAS Acquisition Engine
14

## Slide 15
Thank You
Questions & Discussion
Mashaal Ali
FPGA-Based SBAS Acquisition Engine for L1 C/A Signal